## Slide 1
PeakPilot
Cut a building's peak demand — not the work it has to do
Hackachusetts 2026 · Energy & Climate Tech · Challenge C3
Soham Patwardhan
Same hot evening, same work
19.0 kW
uncoordinated peak
14.0 kW
with PeakPilot — every deadline met
SIMULATED
Notes: Clean power still has to show up at the peak. PeakPilot is an IoT energy coordinator that lowers a building's peak demand without cutting what gets done. Headline: on a simulated hot evening the building peaks at 19 kW uncoordinated; PeakPilot holds it at 14 kW and still meets every deadline.

## Slide 2: The peak, not total energy, is what strains the grid
On a hot evening an EV charger, a water heater and an air conditioner all switch on together
That simultaneous spike is what strains the grid and drives demand charges
Some of those loads could wait — but each still has a job to finish by a deadline
Hackachusetts C3: a more reliable clean energy system — clean power still has to show up at the peak.
19.0 kW
peak demand with no coordination, against a 14 kW building limit
180 min
spent over the power limit
19 min
with the room above the 25 °C comfort limit
SIMULATED
Notes: The peak is what matters for grid reliability. Uncoordinated, our simulated building hits 19 kW against a 14 kW limit, sits over the limit for three hours, and the room still overheats for 19 minutes. All device numbers are simulated.

## Slide 3: Which load can wait, for how long — and still finish?
EV charger
7.2 kW max
Deliver 30 kWh by 07:00
Throttle or pause any minute
Water heater
4.5 kW max
Deliver 9 kWh by 06:30
On/off, 15-min minimum run
Air conditioner
3.5 kW max
Keep the room ≤ 25 °C
On/off, 10-min minimum run
Every device reading and the room's thermal behaviour are SIMULATED. Readings carry an ID and timestamp so a real sensor could implement the same interface later.
Notes: Three simulated devices, each with a different constraint. The EV is continuously throttleable; the water heater and AC are on/off with minimum run times so relays don't cycle every minute.

## Slide 4: Measure, decide, act, explain — every minute
Measure
Each device reports power draw (and room temperature) with an ID and timestamp
Decide
A deterministic controller checks the power limit, deadlines and comfort
Act
Throttle or defer the flexible loads to stay under the limit
Explain
Log a plain-language reason for every action it takes
From the decision log (hot evening, coordinated run):
17:07 ev-1 throttled to fit power limit
17:42 wh-1 heating ON (min run 15 min)
17:57 wh-1 paused to hold building under power limit
Notes: The loop runs once per simulated minute. The explain step is what makes it trustworthy: every throttle, deferral and AC priority decision is written to a log in plain language.

## Slide 5: Who benefits, and how it scales
Building owners
Add EV chargers and other flexible loads under their existing power limit, with every deadline met and every decision explained.
Utilities and grid
Flexible load that moves out of the evening peak, reported in kW and minutes over the limit, including when the limit cannot hold.
Massachusetts towns
351 towns mapped to their utility, landfill renewables from MassGIS. Free and open source (MIT), runs offline with no account.
How it scales
Simulated devices today
Real devices, same reading + command interface
Rust controller on a Raspberry Pi per building
More loads: heat pumps, batteries
Working today: simulation, CI and the Pi image build. Not yet: real devices or a physical Pi.
Notes: Who benefits: building owners who need to add EV chargers and other flexible loads without blowing through their power limit; utilities, who get flexible load moved out of the evening peak and reported honestly; and Massachusetts towns, with 351 towns mapped to their utility. It is free, open source and runs offline. It scales by swapping simulated devices for real ones behind the same interface, with the Rust controller on a Raspberry Pi in each building. Today the simulation, CI and Pi image build work; real devices and a physical Pi are next.

## Slide 6: How Kiro built it: specs, steering, hooks, MCP
Spec-driven
4 Kiro specs (engine, Rust port, LP benchmark, tests): requirements → design → tasks, with tasks traced to requirements.
Steering
4 always-on docs: label SIMULATED, no cost or carbon claims, stdlib-only engine, issue → spec → branch → PR.
Agent hooks
5 hooks: command guard, Context7 docs reminder, Mermaid layout check, diagram suggestions, worktree cleanup.
MCP
chrome-devtools read the live dashboard's accessibility tree and console, leading to PR #14. GitHub MCP ran issues and PRs.
Property tests
Rust proptest, 256 cases per property, found 2 real bugs: missed deadlines marked met, offline devices overshooting.
IDE, CLI, Powers
IDE: specs, code and a multi-agent workflow that shipped PR #12. CLI: UI review → PR #14. Context7 Power for API docs.
Later specs (ML studies, rooftop PV, React plan) were written with Claude Code in Kiro's spec format and steering. Full account: .kiro/KIRO_USAGE.md
Notes: PeakPilot was built spec-first in Kiro. Four Kiro specs cover the engine, the Rust port, the LP benchmark and the test framework, and their tasks trace to requirements. Four steering docs carry the honesty rules into every edit. Five hooks guard destructive commands, remind the agent to check library docs, enforce Mermaid layout, suggest diagrams where they help, and clean up merged worktrees. Through MCP, Kiro checked the live dashboard in a real browser and ran the GitHub issues and pull requests. Rust property tests found two real bugs. Most of the build ran in the Kiro IDE, including a multi-agent workflow that built the optimal benchmark end to end and merged PR #12. One Kiro CLI session reviewed the dashboard UI and led to PR #14. The Context7 Power checked current Streamlit APIs. Later specs were written with Claude Code in Kiro's format, and the repo says so.

## Slide 7
Honest limits, and what's next
What we don't claim
Device telemetry and rooftop PV are simulated
The room model is illustrative, not calibrated
No cost or carbon savings are claimed
The Pi image is tested in CI, not on hardware
Next steps
Real devices behind the same interface
The Rust controller on a physical Pi
Calibrate the room model on real data
More loads: heat pumps, batteries
Try it: github.com/sohampatwardhan/PeakPilot · pip install -r requirements.txt && streamlit run app.py
Thank you. Climate Tech · Challenge C3 · specs, steering and hooks in .kiro/ at the repo root
Notes: PeakPilot makes the tradeoffs of a reliable clean grid visible, honestly. We are explicit about what is simulated and what we don't claim. Next: real devices through the same interface, and the Rust controller on actual Pi hardware. The code, the specs, steering and hooks are all in the public repo under .kiro. Thank you.

## Slide 8: Least-slack-first: closest deadline gets power first
slack
time to deadline − time needed at full power
Lowest slack is served first. At zero slack a task runs flat out — and any breach is logged.
Deterministic: same inputs → same schedule. No randomness, no learned policy.
Equipment-realistic: minimum run times stop relays cycling every minute.
1
Commit forced loads
Base load, offline holds, AC when the room nears 25 °C, water heater mid minimum-run
2
Share the headroom by slack
EV throttles to fit what's left; water heater starts only if its whole 15-min run fits
3
Advance the room
Update room temperature with an RC thermal model, then the next minute
Notes: Each one-minute step is a two-pass allocation. First commit everything that cannot be throttled this minute, then hand the remaining headroom to flexible tasks in order of slack. It is rules-based on purpose, so every decision can be explained and tested.

## Slide 9: Hot evening: 26% lower peak, with every deadline met
Chart: Building demand (kW)
15-minute maximum of simulated building demand, 16:00 → 08:00. EV (30 kWh) and water heater (9 kWh) are fully delivered in both runs.
−26%
peak demand (19.0 → 14.0 kW)
0 min
over the limit (vs 180 uncoordinated)
2 / 2
deadlines met in both runs
24.5 °C
hottest room (vs 25.3 °C, limit 25 °C)
Notes: Same evening, run twice. Red: everything runs at once and the building peaks at 19 kW, over the limit for three hours. Green: PeakPilot holds 14 kW, zero minutes over, every deadline met. The peak dropped because work moved into the night, not because anything was skipped. The coordinated run actually uses 1.2 kWh more AC energy, because it keeps the room under 25 °C.

## Slide 10: Four scenarios, reported as they come out
Scenario (SIMULATED) | Peak: uncoordinated → PeakPilot | Peak cut | Minutes over limit | Deadlines met | Room > 25 °C
Hot evening, 14 kW limit | 19.0 → 14.0 kW | 26% | 180 → 0 | 2 / 2 | 19 → 0 min
Tight limit, 11 kW | 19.0 → 11.0 kW | 42% | 250 → 0 | 2 / 2 | 19 → 0 min
EV offline 18:00–18:45 | 19.0 → 14.3 kW | 25% | 180 → 25 | 2 / 2 | 19 → 0 min
Infeasible: 8 kW, 40 kWh EV due 23:00 | 19.1 → 14.9 kW | 22% | 334 → 291 | 2 / 2 | 25 → 0 min
Same work in both runs. EV and water-heater energy is identical every time. Where the limit still breaks (offline device, impossible deadline), PeakPilot reports the minutes instead of hiding them — a lower peak bought by dropping work would count as a failure.
Notes: All four built-in scenarios. The first two hold the limit outright. The offline and infeasible cases still break the limit, and the table says so in red.

## Slide 11: When the limit can't hold, PeakPilot says so
A device drops offline
The controller can't command the EV charger, so it assumes the charger keeps its last power, reserves that headroom and plans around it.
18:00 ev-1 OFFLINE — holding last
power 6.6 kW, reserving headroom
18:45 ev-1 reconnected; resuming control
Result: 25 min over the limit — disclosed
The limit is impossible
40 kWh into the EV by 23:00 under an 8 kW cap on a 34 °C evening cannot fit. As slack hits zero the EV runs flat out.
18:09 ev-1 deadline forces full
power — exceeding limit
Result: 291 min over, shown in a warning banner
Notes: Two honesty cases. Offline: the controller cannot command the charger, so it reserves its last power and says so in the log. Infeasible: an 8 kW cap with a large early EV deadline. PeakPilot does not fake it; it reports the minutes over the limit. The LP benchmark on the next slide confirms no schedule could have stayed under 8 kW.

## Slide 12: How close to optimal? A perfect-foresight lower bound
Chart: Peak demand (kW)
| Hot evening (14 kW) | Tight limit (11 kW) | EV offline (14 kW) | Infeasible (8 kW)
Uncoordinated | 19.03 | 19.03 | 19.03 | 19.09
PeakPilot | 14 | 11 | 14.29 | 14.91
LP lower bound | 6.03 | 6.03 | 6.03 | 10.53
One linear program over the same 960 one-minute steps, solved with SciPy's HiGHS in ~0.03 s. It must do the same work: every deadline, the offline hold, the room ≤ 25 °C.
A lower bound: it sees the whole evening in advance and lets on/off devices run at any power.
The gap is large on easy limits because PeakPilot aims for the limit you set, not the minimum possible peak.
At 8 kW the bound is 10.5 kW — proof that no schedule could have held that limit.
Notes: To check the scheduler, the same scenario is written as one linear program and solved for the lowest peak any schedule could reach. It is deliberately framed as a lower bound: perfect foresight and relaxed on/off rules. Its most useful job is the infeasible case, where it proves the 8 kW limit was impossible. No cost or emissions claims follow from the gap.

## Slide 13: Massachusetts context, kept apart from the simulation
Pick a town
See its electric utility and landfill renewables
Simulate a building
Compare coordinated vs uncoordinated
Public fact (MassGIS) · Simulation (SIMULATED)
351
towns mapped to their electric utility
116
renewable projects at MA landfills (status, reported capacity)
Bundled CSV snapshot saved 2026-10-18 — no network needed. Source and date are shown in the app.
What this data does not establish
Tariffs, live grid demand or capacity
Price or carbon intensity
Which generator supplies a building
Reported landfill MW is not generation
Notes: PeakPilot adds a local planning layer: pick a town, see its utility and listed landfill renewable projects. MassGIS describes local infrastructure; the simulation tests building-level coordination. We never infer generation from installed capacity.

## Slide 14: Built to be checked: one engine, many tests
One pure-stdlib engine
All control logic lives in peakpilot/engine.py. The Streamlit dashboard is a thin view and never re-implements the loop.
Rust port for a Raspberry Pi
Static arm64 binary in a 0.8 MB image. Matches Python's JSON output exactly on 130 cases in CI. Not yet run on a physical Pi.
Tested end to end
180 pytest tests with a 90% coverage gate in CI, plus Hypothesis property tests in Python and proptest in Rust.
Rooftop PV with MPPT
Optional SIMULATED array. Perturb-and-observe tracking captures 99.97% of the true maximum power point; the limit applies to net grid import.
Notes: The engine is the single source of truth and imports only the Python standard library, so it is portable and deterministic. A Rust port targets a Raspberry Pi that would sit in the building; CI checks both engines give identical output on 130 cases. 180 pytest tests run with a 90% coverage gate. The newest addition is an optional simulated rooftop PV array whose inverter tracks its maximum power point, so the limit applies to net grid import.